## Slide 1
ECE4078 Intelligent robotics
Lab 2-2: Kal Backman & Tina Wu

## Slide 2
Milestone 2
Milestone is all about SLAM
Your task is to estimate the position of all ArUco markers within the arena
Task 1: Wheel calibration (Week 3)
- Objective is to calculate the wheel radius and the distance between both wheels
Task 2: Camera calibration (Week 3)
- Objective is to calculate the intrinsic parameters of the camera
Task 3: SLAM (Week 4)
- Estimate the position of ArUco markers in the environment using an extended Kalman filter (EKF)
- Have to modify 2 main files:
- “robot.py”: “predict()” and “update()” functions
- “ekf.py”: “derivative_drive()” and “covariance_drive()” functions
- Your solution should automatically generate “slam_map.txt” to evaluate your estimates

## Slide 3
Extended Kalman filter
When to use a Kalman filter:
- Sensor fusion
- Want to apply dynamics + sensor measurements
There are two main steps
1: Prediction step – We apply a dynamic model to estimate what the state should look like
given our previous state. Eg: Knowing the velocity of an object, we can guess what it’s position will be 1 second into the future
2: Update step – Correcting / updating the estimate of the current state with observations from sensor readings
Eg: We use a GPS to get a direct observation of what the position actually is
But how much should we “update” our state given an observation?
What if we have multiple sensors (Camera/GPS/LIDAR) which one should we use?
Kalman filters are a probabilistic algorithm to estimate a given state (i.e. mean and covariance)
- If we are confident in our dynamic model, then we shouldn’t rely heavily on noisy observations
- If we have a noisy sensor (GPS), then we should weight it less than an accurate one (LIDAR)

## Slide 4
Extended Kalman filter example
We want to track the position of an object that has an accelerometer and a GPS attached
Accelerometer: - High update rate
- Prone to drift after successive time integrations
GPS:
- Slow update rate
- Immune to drift
- Not accurate
3 states:

## Slide 5
Extended Kalman filter example
Prediction step:
Step 1: Apply dynamics
Step 2: Calculate Jacobian of dynamics
Step 3: Estimate uncertainty
This matrix is denoted as “A” in the lecture slides however many other people may denote this as “F”
Covariance matrix of the states, this is also commonly denoted as “P”
This matrix represents your uncertainty in the process / dynamics.
Commonly referred to as “Q”, and is normally tuned. There is an alternate form which uses where V is the Jacobian of the states with respect to “” from the lecture slides.

## Slide 6
Extended Kalman filter example
Observation / correction / update step:
Step 1: Calculate error of observation and prediction
Step 2: Calculate Jacobian of error (multiply by -1)
Step 3: Update Kalman gain and states
X = + K Y
This matrix is denoted as “C” in the lecture slides however many other people may denote this as “H”.
For extended Kalman it is calculated as
This matrix represents your uncertainty in the observation
and is normally tuned. “” is also denoted as “S”
Is the Kalman gain and it acts as a step size as to how much you should update your states based on an observation
The error term Y is more generally denoted as where z is the sensor measurement and h( ) is a function that allows you to compare the state with the sensor measurement

## Slide 7
Milestone 2 submission
M2 deadline has been extended an extra week to accommodate Kalman filters not being covered in the lectures before the final M2 lab sessions
M2 due before: Monday 30th August 12:00 PM
Submission guidelines:
When submitting your milestones, the demonstrators should only have to download your .zip file, extract the contents and run a script
When submitting your milestones please include:
- All files that are essential to run your solution
- This includes the pibot.py / images for the GUI / any other scripts provided to you
- A ReadMe.txt file that should include:
- Information on how to setup your solution (additional libraries to install)
- How to run your solution (What command should we run? What are the controls?)
- If you have implemented any additional features please explain them
Please do not include any other file that is not required to run your solution
e.g. default ReadMe.md / images associated with the default ReadMe.md